## Slide 1: Fundamentals of Remote Sensing

## Slide 2: Outline
• Fundamentals of Remote Sensing
• Satellites and Sensors
  ⁃ Types
  ⁃ Resolution
• Satellite Data Processing Levels
• Projections and Coordinate Systems
• Advantages and Disadvantages of
Remote Sensing
• Remote Sensing Terminology

## Slide 3: Introduction
What is remote sensing?
Remote sensing is obtaining information about an
object from a distance.
Photography is a very common form of remote sensing.
There are different ways to collect data, and different
sensors are used depending on the application.
Some methods collect ground-based data, others airborne or spaceborne.
What information do you need?
How much detail?
How frequently do you need the data?

## Slide 4
What is Remote Sensing?
The energy Earth receives from the sun is called electromagnetic radiation.
• Radiation is reflected, absorbed, and emitted by the Earth's atmosphere or surface, as shown by the figure on the left.
• Satellites carry instruments or sensors that measure electromagnetic radiation reflected or emitted from both terrestrial and atmospheric sources.
• With calibrated instruments, scientists can measure the height, temperature, moisture content (and more) for nearly every feature of the Earth’s atmosphere, hydrosphere, lithosphere, and biosphere.

## Slide 5
What is Remote Sensing?
The electromagnetic spectrum is simply the full range of wave frequencies that characterizes solar radiation.
Although we are talking about light, most of the electromagnetic spectrum cannot be detected by the human eye. Even satellite detectors only capture a small portion of the entire electromagnetic spectrum.

## Slide 6
Different materials reflect and absorb different wavelengths of electromagnetic radiation.
• You can look at the reflected wavelengths detected by a sensor and determine the type of material it reflected from. This is known as a spectral signature .
• In the graph on the left, compare the relationship between percent reflectance and the reflective wavelengths of different components of the Earth’s surface.

## Slide 7
Vegetation
• Certain pigments in plant leaves strongly absorb wavelengths of visible (red) light.
• The leaves themselves strongly reflect wavelengths of near -infrared light, which is invisible to human eyes.
• As a plant canopy changes from early spring growth to late -season maturity and senescence, these reflectance properties also change.
Since we can't see infrared radiation, we see healthy vegetation as green.

## Slide 8
Water
• Longer visible wavelengths (green and red) and near infrared radiation are absorbed more by water than shorter visible wavelengths (blue) – so water usually looks blue or blue-green.
• Satellites provide the capability to map optically active components of upper water column in inland and near-shore waters.

## Slide 9
Atmosphere
• From the sun to the Earth and back to the sensor, electromagnetic energy passes through the atmosphere twice.
• Much of the incident energy is absorbed and scattered by gases and aerosols in the atmosphere before reaching the Earth’s surface.
• Atmospheric correction removes the scattering and absorption effects from the atmosphere to obtain the surface reflectance characterizing surface properties.

## Slide 10: Satellites and Sensors
Satellites carry sensors or instruments. The names of sensors are usually acronyms that can include the name of the satellite.

## Slide 11: Satellite Characteristics
● Orbits: Polar/Non-Polar Orbit vs. Geostationary
● Energy Source: Passive vs. Active
● Solar and Terrestrial Spectra: Visible, UV, IR, Microwave...
● Measurement Technique: Scanning; Non-Scanning; Imager; Sounders ● Resolution Type and Quality: Spatial, Temporal, Spectral, Radiometric ● Application: Weather, Ocean Color, Land Mapping, Air Quality, Radiation Budget, etc.

## Slide 12: Satellite Sensors
1. Passive Sensors
• Passive remote sensors measure radiant energy reflected or emitted by the Earth atmosphere system or changes in gravity from the Earth.
• Radiant energy is converted to biogeophysical quantities such as temperature, precipitation, and soil moisture.
• Examples: Landsat OLI/TIRS, Terra MODIS, GPM GMI, GRACE, etc.

## Slide 13: Satellite Sensors
2. Active Sensors
• Active sensors provide their own energy source for illumination
• Most active sensors operate in the microwave portion of the electromagnetic spectrum, which makes them able to penetrate the atmosphere under most conditions and can be used day or night.
• Have a variety of applications related to meteorology and observation of the Earth's surface and atmosphere.
• Examples: Laser Altimeter, LiDAR, RADAR, Scatterometer, Sounder
• Missions: Sentinel -1 (C -SAR), ICESat -2 (ATLAS), GPM (DPR)

## Slide 14: Advantages of Remote Sensing
Provides information where there are no ground -based measurements.
• Provides globally consistent observations.
• Provides continuous monitoring of our planet.
• Earth systems models integrate surface -based and remote sensing observations and provide uniformly gridded, frequent information of water resources data parameters.
• Data are freely available and there are web -based tools for data analysis.

## Slide 15: Disadvantages of Remote Sensing
It is very difficult to obtain high spectral, spatial, temporal, and radiometric resolution all at the same time.
• Large amounts of data in a variety of formats can lead to more time and processing.
• Applying satellite data may require additional processing, visualization, and other tools.
• While the data are generally validated with selected surface measurements, regional and local assessment is recommended.

## Slide 16: Applications of Remote Sensing
- Agriculture monitoring - Urban planning - Environmental monitoring

## Slide 17
THANK YOU